## Slide 1: A Gen-2 calibration borehole with the U.S. Rapid Access Ice Drill (RAID)? Jeff Severinghaus (University of California, San Diego) John Goodge (University of Minnesota, Duluth)

## Slide 2: Why rapid-access ice drilling?
Conventional ice coring takes ~5 yr, $50M
High risk of not getting target ice
Most new science targets are near the bed
(e.g. last interglacial, >1 million yr old ice, subglacial biology, bed and till properties)
Borehole logging is a new science frontier
Geophysical instruments, heat flow probes need boreholes

## Slide 3
new concept for exploring deep ice & bedrock
ability to go deep (2500-3300 m)
cuts entire ice sheet in two days
rapid mobility on sleds allows for many holes
creates observatory of legacy holes
potentially transformative with new multi-disciplinary opportunities
Rapid Access Ice Drill (RAID)
Notes: in 2012 started a collaboration with an ice scientist to design and construct a new drilling platform to...
2500 m = 8000 ft
Tom Cruise for scale

## Slide 4: Closed-loop fluid circulation to remove ice chips: the key to fast drilling
ICE
3000 m
borehole
chips
Rotating drill pipe
Drill fluid

## Slide 5: Successful RAID test at Minna Bluff, Antarctica (2019-2020)

## Slide 7: Ice core taken by RAID just above bedrock, Minna Bluff Jan. 2020
Age of ice: ~15,000 yr BP
Air-based (δ18Oatm) dating
Successful borehole optical dust log for rapid ice dating (Ryan Bay, Delia Tosi)

## Slide 8: One meter deeper…

## Slide 9: 0.5 meter deeper still….

## Slide 10: Limitations of RAID
Designed for speed, not for perfectly vertical hole. Borehole can be up to 10 deg off vertical
Cannot penetrate wet bed (for bio stewardship)
Five ski-mounted modules require 3-5 Challenger tractors to pull, depending on snow conditions & grade
QUESTIONS?