## Slide 1: Cryoscope A technology pathfinder for time domain astronomy in the NIR
Roger Smith and Mansi Kasliwal
The convergence of many new technologies will soon enable high cadence surveys of the infrared sky for the first time. We describe a pathfinder telescope currently under construction, which will demonstrate a technology for imaging over a field of view two orders of magnitude greater than previously achieved in the thermal infrared. The novel optical design not only delivers diffraction limited image quality over large fields, but its double meniscus corrector serves as the entrance window to a fully cryogenic optical path that assures low thermal background in spite of the large field of view. We describe the window manufacturing and support strategies which allow scaling to apertures larger than a meter, and the various methods to prevent ice precipitation. A new, cheaper, growth process for large format infrared detectors is showing promise of making a 600 megapixel NIR focal plane feasible. High speed direct drive telescope mounts, now commercially available, will be upgraded to provide the vibration isolation necessary to take advantage of the exquisite seeing.
SCAR AAA 2021

## Slide 2: To catch transients in NIR
DEEP
WIDE
FoV = 0.6 deg2
= Current record
VISTA @ ESO
DARK
(Low sky background)
49 deg2 every1000s with SNR>5 for magnitude 23.3 at 2.3<λ<2.55µm

## Slide 3: 200 times wider field
DEEP
WIDE
FoV = 47 deg2
24K * 24K pixels
DARK
Cheaper IR detectors developed by NSF-ATI

## Slide 4: Smaller pixels & darker sky
DEEP
1.2 m aperture
1 arcsec pixel
Diffraction limited
WIDE
FoV = 47 deg2
24K * 24K pixels
DARK
Dark sky @ 2.4µm
Cold window (slightly above ambient)
Dome C
30m tower

## Slide 5: Optics to match good seeing
DEEP
1.2 m aperture
1 arcsec pixel
Diffraction limited
WIDE
47 deg2 FoV
24K * 24K pixels
Scan whole night sky in less than a “day”…
DARK
Dark sky @ 2.4µm
Cold window (slightly above ambient)
Cryogenic optical path
New Optical design
Image stabilizing telescope mount

## Slide 6: Cheaper large format IR detectors: ✔︎ good QE
NSF-ATI grant has funded development at Raytheon of MBE-on-silicon process for making large NIR detectors 4x cheaper. (PI: Don Figer)
~80% QE in K_dark passband
Peak of QE curve can be tuned for peak in middle of passband.
27e- read noise prior to multiple sampling.
Kdark passband

## Slide 7: Low dark current. Tight noise distribution
✔︎ Require < 10 e-/s ︎
✔︎ Require < 31 e-

## Slide 8: Hybridize to SC 4Kx6K ROIC
4K*6K Readout IC by Sensor Creations Inc
  Funded by NASA SBIR grant (via WFIRST)
  Currently under test
Cryoscope will deploy 6x4 mosaic
  24K*24K pixels
  Instantaneous Field of View = 49 deg2
  Beam obstruction by 6x4 mosaic is only 8%
10 µm pixels  1.031 arcsec/pixel
  telescope focal length = 2.0 m
  1.2m aperture
  f/1.66
   FWHM at diffraction limit = 4.2 µm
43.795 mm
71.12 mm
8’’ wafer

## Slide 9: Air glow lines
Wavelength 9µm)
Log intensity
K_dark
2.26
Optimum passband starts at 2.26 µm

## Slide 10: South Pole - atmospheric transmission
Lower water column at Dome C (higher altitude, lower temperature)
South Pole: 2835 m
Dome C: 3233 m
Dome A: 4093 m
K_dark

## Slide 11: Black body power density
Telescope on Mauna Kea (277K)
Telescope Dome C @30m (233K)
Sky over Dome C ? (173K)
Reduced emission from telescope helps but very widefield designs have higher emissivity thus need to be as cold as sky.

## Slide 12: Fucik Telescope
Diffraction limited
  Excellent image quality even at f1.2 and 100 sq.deg.
All fused silica corrector  scalable to large aperture.
Arizona Mirror labs are developing glass slumping to fabricate large menisci economically.
  Similar lenses are used in prime focus correctors.
Shorter than a Schmidt  smaller primary for given aperture and FoV

## Slide 13: Negligible aberrations !
Spots are much smaller than 18 µm pixel
RMS radius < 1.2 µm
diffraction limit
Pathfinder
4.06 deg x 4.06 deg field of view
260mm aperture at f/2
With aberrations, all field points
18µm pixel for pathfinder

## Slide 14
Dome C

## Slide 15: Why a cryogenic telescope ?
Usual measures to block rays from warm telescope limit FoV.
…but without re-imaging optics and cold Lyot stop, telescope emissivity is closer to 1 than the ~2% emissivity of optics.
At top of inversion layer (25-30m above ice), T= ~230 K  not cold enough
We really want telescope temperature < sky temperature < 200 K.
2nd corrector element of Fucik optical design can serve as window, so full optical path can be cryogenically cooled.

## Slide 16: Cryoscope pathfinder
IR Labs ND5 for pre-cool with LN2
Pulse Tube cryocooler
Detector controller
STA Archon-DC
Vacuum Interface Board
Thermal isolator,
G10 cylinder
Conductive thin Al cylinders
= structural support
+ light seal
Diamond turned Al primary
~75% light weighted
Narcissus baffles return most thermal radiation to window
One more Narcissus baffle to be added here
Field flatteners [2]
Convex window
Concave corrector
Zeolite desiccant [6]
Warm baffles
outside FoV radiatively heat first element
Commissioning in April 2022
Detector
at prime focus
Thermal standoff for front baffle

## Slide 17: Detector test system assembled
This is a lab test dewar, not Cryoscope.
Allows early testing of components to be used in Cryoscope: controller, wiring and detector.
Readout waveforms in development now.
Tests Cryoscope detector control software.

## Slide 18: Vacuum Interface board
Connector for flex circuit to detector,
Routed inside spider
Preamps
(in vacuum)
Connects directly to detector controller boards
Smooth surface for O-ring contact (both sides)
Flexible section

## Slide 19: Window Stress Analysis
FoS =2 ✔︎
FoS =35 ✔︎
Tension
Compression
Factor safety = 35
Tangential support by silicone gasket keeps glass in compression
Nusil CV2566 gasket
Titanium for CTE match

## Slide 20: >80% of radiation from window is returned to window (non-sequential ray tracing)
Source: window radiates light into π2 steradians equally
Config | Total Input | Total Missed* | Total Enters Window | Total Detector** | Total Exiting Window and Reflected Off Baffles** | Baffle 1** | Baffle 2** | Baffle 3** | Baffle 4** | Baffle 5** | Baffle 6**
Cone Baffles | 1.0000 W | -- W | 0.3990 W (100%) | 0.0009 W (0.2%) | 0.1758 W (44.1%) | 0.1276 W (32.0%) | 0.0246 W (6.2%) | 0.0132 W (3.3%) | 0.0072 W (1.8%) | 0.0020 W (0.5%) | 0.0013 W (0.3%)
Elliptical Baffles | 1.0000 W | -- W | 0.3990 W (100%) | 0.0005 W (0.1%) | 0.1990 W (49.9%) | -- | -- | -- | -- | -- | --
Mixed Baffles E(2,3,4);C(1,5,6) | 1.0000 W | -- W | 0.3990 W (100%) | 0.0005 W (0.1%) | 0.1569 W (39.3%) | 0.1270 W (31.8%) | 0.0267 W (6.7%) | -- | -- | 0.0020 W (0.5%) | 0.0012 W (0.3%)
Three points of measurement: front/back side of window and detector
Since making the above table, this number has been raised to 80%
with addition of baffle here
Further improvement is anticipated by filling this gap

## Slide 21: Neglible out-of-field light scatters onto detector (non-sequential ray tracing)
Config | Total Input | Total Missed* | Total Enters Window | Total Detector** | Total Exiting Window and Reflected Off Baffles** | Baffle 1** | Baffle 2** | Baffle 3** | Baffle 4** | Baffle 5** | Baffle 6**
Cone Baffles | 1.0000 W | 0.3076 W | 0.4499 W (100%) | 0.0363 W (8.1%) | 0.2361 W (52.5%) | 0.0099 W (2.2%) | 0.0170 W (3.8%) | 0.0284W (6.3%) | 0.0487 W (10.8%) | 0.0710 W (15.8%) | 0.0584 W (13.0%)
Elliptical Baffles | 1.0000 W | 0.3076 W | 0.4499 W (100%) | 0.0017 W (0.4%) | 0.4024 W (89.4%) | -- | -- | -- | -- | -- | --
Mixed Baffles E(2,3,4);C(1,5,6) | 1.0000 W | 0.3076 W | 0.4499 W (100%) | 0.0017 W (0.4%) | 0.3764 W (83.7%) | 0.0086 W (1.9%) | -- | -- | -- | 0.0749 W (16.6%) | 0.0565 W (12.6%)
*Light that does not enter corrector lens 1.
** Percent calculated from total flux entering the window.
Two points of measurement: front side of window and detector
Detector Flux
Flux Exiting Window
Flux Entering Window
Source: sends light equally into 2.8° - 15°
1
2
3
4
5
6

## Slide 22: Dry air supply
Ice
25 m boundary layer
1 C/m temperature rise
-65 C
-40 C
Blower
Wide flat duct equilibrates air to ambient as it rises
Relative humidity drops significantly as air equilibrates to higher ambient T
Inlet
RH=100%

## Slide 23: Image stabilizing telescope mount
Must isolate telescope from vibration of tower:
Use low friction bearings rated for low temperature.
Direct drive torque motors, so coupling is magnetic only.
Active feedback from bright stars provided by sensor using sub-array readout.
Use optical encoders only during slews.
Torque motor in telescope mounts by planewave.com
Custom bearings and servo are under discussion with Planewave.
Masters Student in Robotics at JHU is planning to test cryogenic bearing and develop image stabilizing servo

## Slide 24: Conclusion
Cryoscope will validate:
New optical design (diffraction limited over wide field)
Cryogenic optical path
Low sky background (when telescope emission is suppressed).
Window temperature control (narcissus baffle performance)

## Slide 25: ✔︎ Good well capacity ✔︎ Low Interpixel Crosstalk
%
Full well > 160 ke-
This non-linearity is low for NIR detector

## Slide 26: Background: sky + telescope
Low sky temperature pushes rising edge of blackbody curve beyond 2.55 µm.
Reduced emission from telescope helps but very widefield designs have higher emissivity thus need to be colder.
Sky is probably colder than this
We will eliminate this

## Slide 27: Dome C seeing
These numbers are for 30m above ice.
75% of time, seeing is better than Cryoscope diffraction limit (0.4”).
Full potential when mounted on tower.
Pathfinder (0.26m aperture) is small enough to be mounted on existing building.

## Slide 28: Optical tolerances are quite loose
 Manufacturing tolerances
 Mounting, alignment and flexure tolerances

## Slide 29
3D printed stainless steel lens holder with integrated radial springs.
The axial spring plate (not shown at right) is also printed.
Temporary screws inserted here retract springs to facilitate lens installation
Flex cable hidden in channel in spider
2nd narcissus baffle
Detector