## Slide 1
The antenna system of COSMO
(COSmic Monopole Observer)
Elenia Manzan
Università degli Studi di Milano
SCAR AAA 2021
08/09/2021

## Slide 2
Aims at measuring the isotropic y-distortion of the CMB spectrum
The current state-of-the-art is , from COBE-FIRAS and TRIS
COSMO forecasted sensitivity:
Site: Concordia station, Antarctica
The COSMO experiment
08/09/2021
Image: COSMO collaboration
SCAR AAA 2021

## Slide 3
The COSMO experiment
Differential, cryogenic Martin-Pupplett Fourier Transform Spectrometer (FTS)
Reference Blackbody
Focal planes + band-pass filters
FTS
2 Focal planes: 18 multimoded feed-horns + KID bolometers
Band: 120-300 GHz (limited by the atmospheric window)
The cryostat can be tilted and a spinning wedge mirror performs fast sky scans
08/09/2021
SCAR AAA 2021

## Slide 4
The antenna system
08/09/2021
SCAR AAA 2021

## Slide 5
Overview of the antenna system
Array 1 band: 120-180 GHz
Array 2 band: 210-300 GHz
Antennas: smooth-walled feed-horns
Made in aluminum with CNC milling
3x3 feed-horn arrays
Multimoded feed-horns instead of traditional single-mode horns
08/09/2021
SCAR AAA 2021
[measures in mm]

## Slide 6
Multimode propagation principle
Band | Waveguide diameter | # modes
120-180 GHz | 4.5 mm | From 10 to 19
210-300 GHz | 4 mm | From 23 to 42
A hollow circular waveguide supports TE and TM mode propagation.
TE11
TM01
TE21
TM11
TE01
TE31
TM21
TE41
TE12
TM02
Band | Waveguide diameter | # modes
120-180 GHz | 1.47 mm | 1
210-300 GHz | 1 mm | 1
Single-mode antenna
Multi-mode antenna
08/09/2021
SCAR AAA 2021
Cut-off frequency

## Slide 7
Multimoded receivers (antenna+detector) have a higher signal-to-noise level:
Multimoded antennas can illuminate the cryostat aperture (or telescope) more uniformly than single-mode ones.
Multimode propagation advantages
08/09/2021
SCAR AAA 2021
The beam pattern describes the antenna performance, i.e. the angular distribution of emitted/received power in farfield condition.
Multimoded beam pattern are flatter than single-mode ones along the antenna axis.
150 GHz

## Slide 8
Aperture window
Focal planes + band-pass filters
The antenna design in details
The antenna design is the best trade-off between
The multimode requirement on the circular waveguide: fixed waveguide diameter
The mechanical constraint on the antenna aperture: aperture 24 mm
The optimization of the antenna directivity inside
  the cryostat aperture window, seen under a angle (f/# 3.3)
08/09/2021
SCAR AAA 2021
Band | Waveguide diameter
120-180 GHz | 4.5 mm
210-300 GHz | 4 mm

## Slide 9
The low-frequency array
Profile: 4.5 mm circular waveguide + platelet Winston cone
08/09/2021
SCAR AAA 2021
[measures in mm]

## Slide 10
The high-frequency array
08/09/2021
SCAR AAA 2021
Profile: 4 mm circular waveguide + linear profile
[measures in mm]

## Slide 11
Low-frequency array
Forecasted broadband performance
08/09/2021
SCAR AAA 2021
Fixed plane
Fixed plane
High-frequency array
Fixed plane
Fixed plane

## Slide 12
High-frequency array
Low-frequency array
Forecasted broadband performance
08/09/2021
SCAR AAA 2021
Fixed plane
Fixed plane
Fixed plane
Fixed plane
Half-power level
Cryostat aperture edge

## Slide 13
High-frequency array
Low-frequency array
Forecasted broadband performance
08/09/2021
SCAR AAA 2021
Fixed plane
Fixed plane
Fixed plane
Fixed plane
Half-power level
Cryostat aperture edge
To compensate for the slow decrease at the edge of the aperture and further away
    the inside of the cryostat is covered with an absorber
    the instruments are kept at a very low temperature ( K)

## Slide 14
Summary
The antenna system of COSMO consists of two arrays of nine smooth-walled feedhorns
The 120-180 GHz array is made of platelet Winston cones
The 210-300 GHz array is made of linear horns
The feed-horns are multimoded
The design is the best trade-off between mechanical and electromagnetic requirements, with side lobes below -15 dB and HPBW (Half Power Beamwidth) between and
The arrays are made in aluminum through CNC milling
08/09/2021
SCAR AAA 2021

## Slide 16
Back-up slides

## Slide 17
TE11
TM01
TE21
TM11
TE01
TE31
TM21
TE41
TE12
TM02
Multimode propagation principle
A hollow circular waveguide supports TE and TM mode propagation.
Solving the Helmholtz equation for a TE (or TM) wave and applying transverse boundary conditions shows that each mode has a cut-off frequency
, where is the n-th root of
, where is the n-th root of
If the mode is evanescent
If the mode propagates
Bessel function

## Slide 18
TE11
TE12
Each mode has its own beam pattern. A few examples:
Some beams are symmetric w.r.t. the azimuthal angle , some are not.
TE31
Individual mode beam pattern

## Slide 19
The COSMO antenna profiles
150 GHz array: platelet Winston cone
255 GHz array: linear horn

## Slide 20
Mode modification
From this
To this
Do this but in a controlled fashion

## Slide 21
Mode conversion
From this
To this
What I want to do:
How I can do it:
Credit:
Do this but for several modes