## Slide 1: Time-of-Arrival Detection (TOAD) Array
Perry Sandstrom for ARA Collaboration
July 23, 2015

## Slide 2: Basic Idea of TOA Detector Array
Cover large area with dense array of 50m deep RAM-drilled holes (15min/hole)
Multiple holes involved in each detected GZK event
Example: 64km^2 array of 1600 holes with 200m spacing => $2M-$5M of hardware
(1) string per hole; (2-4) transient sensors per string (Vertical spacing= 10m)
Each sensor is an integrated Vpol antenna/electronics PCB
Each sensor provides RF envelope to surface for TOT or other digitizer
Each sensor has azimuthally uniform detection pattern
Determine RF elevation independently at each hole
Real-time downward rejection at each hole
Mass-produced array components (approximately 4 configuration items)
Compatible geometry for co-location with CR surface array

## Slide 3: GZK Field Contours Confirmation by Spatial Signature (1km deep, horizontal event shown)
E max (r)
~E max (r) /2
~E max (r) /10
1 km
Transient
Sensor
Elements
(333m spacing shown)
Event
“Imaging” technique proposed by Gusev and Zheleznykh ~1983

## Slide 4: Combined Surface/CR and Radio Array
2km
200m

## Slide 5: Conceptual Transient Sensor Array Configuration & Power Requirements
Hole
Dry, 4” dia.
TDA 1
20m Depth
TDA 2
50m Depth
SPA
Surface
Processor
Assembly
Data Collection /
Power Distribution
d
(AZ.)
20 km
20 km
Example
“Kilocube”Array
1000 km3
~10.8KW total
Hole with (2-4) transient sensors
~3Watts per hole
Array of holes
180Watts/Row
s
(EL.)
Daisy Chain
Wired Power
For Entire Row
e.g. #12, RG8, RG11

## Slide 6: TDC-Based SPA Block Diagram (prelim) (Arbitrary Elevation Gating- Two TDA channels shown)
Discriminator
Discriminator
Envelope
Signals
Upper
TDA
Lower
TDA
Threshold
START
STOP CH1
STOP CH2
TOT
Time-Digital
Converter (TDC)
4-fold stops/ch
65ps bin size
Min 200ns window
ALU
Hit Processor
Hit Buffer
Elevation
& Coinc.
Fine Time
Data
Coarse Time
from Master clock
TDC
Settings
Buffered Hit Data
Serializer
Get Data
Master Clock Pair
Data Pair
Slow Control
Pair
TDOA
Adjacent
SPAs

## Slide 7: Downward Rejection via Priority, Coincidence Real-Time, Simplest “Elevation Gating”
TDA (A)
TDA (B)
A
B
A
B
A
B
d ~30m
Lowest Detectable Neutrino Trajectory
(93 degree zenith)
Surface Transients
Reject
Accept
Accept
Time Difference Of Arrival (TDOA)
Highest Detectable Neutrino Trajectory
(36 degree zenith)
Surface Processor
Notes: Blue box is simple F/F based elevation gate (probably inside sensor A)

## Slide 8: Programmable Elevation Gating
Horizon Reject
Discriminator threshold can be
lower than transients from surface
without overwhelming data handling
Sky Scan
Cosmic Ray and
calibration studies
Allows real-time rejection or acceptance of arbitrary elevation ranges

## Slide 9: Elevation Gating for GZK
Peak Vertical Field Strength
In Detector Array
Earth
Axis
Cutoff due to
Depth of Sensor Plane
Earth Limb
Cutoff
Horizon
Polarization
Response
Corresponding
Elevation Gating
(RF elevation angle)
Earth/Sensor/Array
Axis
Vpol Array Peak Response to GZK
(neutrino zenith angle)

## Slide 10: Time Resolution Requirements for 1 degree broadside accuracy
ANITA
Transient Sensor -Elevation “s”
AURA & ARA
Transient Sensor -Azimuth “d”
Waveform- Capture Systems
~5-10 kilobyte
per hit/station
TOA System
~10 byte
per hit/hole
Air
Ice

## Slide 11: Transient Detector Assembly (TDA) Primary configuration item for TOA Detector System
23dB Gain
0.9dB NF
80dB log Detector
Antenna
Input
Bias-T
3.3V
Reg
V+
Pdis ~.5W
LNA1&2:
- Active Antenna sensor for Time Of Arrival (TOA)
- Envelope signals sent to surface
- “Common Mode” design possible for multiple TDAs on single cable
100MHz-
800MHz
Band Pass
450MHz
Notch
Envelope
Output
Transient Detector Assembly

## Slide 12: TDA vs. Waveform Capture Low-level Sensitivity
With infinite persistence to show electronics noise
141uVp-p
Input Stimulus
TDA Response
AURA Front end
(similar to ARA)
Min TDA Stimulus for:
~100% detection
~0% false hits
200mVp-p
Stimulus
Att -63dB

## Slide 13: TDA Development
2007
2008
2008
2009
2010

## Slide 14: Envelope / TDA Proof-of-Concept Testing South-Pole 08-09
Ignition noise transients from idling snowmobile
Snowmobile was approximately 100m distance from ICL.
Snowmobile was perpendicular with West tower.
Signals as acquired by ic-scope-ag1
Time Delay=20ns W-E, consistent with Angle-of-Arrival (AOA)
Transient
Wavefront
Snowmobile
(transient source)
West
tower
East
tower
View of snowmobile
from ICL Door
Delta t =20ns

## Slide 15: SATRA Deployment Pictures

## Slide 16
Hagar Landsman IceCube radio extension Status and results ARENA 2010
(due to ice-firn refraction)

## Slide 17
Hagar Landsman IceCube radio extension Status and results ARENA 2010

## Slide 18
18
Ray tracing from pulser to SATRA
Source
at -250m
Bottom antenna
-35m
Top antenna
-5m
Depth [m]
XY separation [m]
surface
Direct rays
Reflected rays
Measured time differences:
Time differences between direct rays
And between direct and reflected rays can be calculated
Hagar Landsman IceCube radio extension Status and results ARENA 2010

## Slide 19: Limits for N(z) found using SATRA
Based on set of hit time differences between antennas
and between primary and secondary hits on the same antenna,
a limit on the index of refraction model can be obtained.
Systematics taken into account: n_deep, Geometry, timing resolution, WF features
Hagar Landsman IceCube radio extension Status and results ARENA 2010

## Slide 20: Rapid Air Movement (RAM) Drill

## Slide 21: “KiloCube” Conceptual 1000 km3 Time-Of-Arrival Array
~ Thousand+ holes/sensor strings
~ $1K-$3K for each string
~ 50m hole depth
~ 200m hole spacing
~ a few watts / string
Conic Sections at intersection of Askaryan profile and sensor plane.
(Distortion by ∆Nice-firn not modelled)
20 km x 20 km firn array
Refraction of Askaryan cone leaving firn not shown
E max (r)
~E max (r) /2
~E max (r) /10
Event Confirmation by:
-spatiotemporal signature
-up-going waves at each string
-coincidence over large area
Notes: 16km x 20km

## Slide 22: Cost and Power Estimates for 20km x 20km (1000m3) Array
Grid Spacing | Total # holes | Array Cost ($4K /hole) | Array Power (2.5W /hole)
200m | 10000 | $40 M | 25 kW
333m | 3600 | $14.4 M | 9.0 kW
500m | 1600 | $6.4 M | 4.0 kW
1000m | 400 | $1.6 M | 1.0 kW
Instrumentation Cost /hole
TDA 1 w/cable $500
TDA 2 w/cable $500
SPA $1K
Data/Power Link $1K
Deployment Cost/hole
Fuel (20gal) $300
0.2 operator-days $700
Total Incremental
cost per hole: $4K
DAQ: $1M Project Overhead: x ~1.5
R&D: $2M
Drill(s): $1M ea.
Additional hardware-related costs:

## Slide 23: Things to remember with TOAD setup:
Orders of magnitude less complexity and cost per hole
Orders of magnitude faster and cheaper hole drilling
Depth shadowing “doesn’t matter” with dense array
Event confirmation includes uniquely characteristic spatial signature
Vpol sensors are responsive to strongest part of cone
Vpol sensors allow narrower (e.g. RAM drilled) holes
RAM drill allows more uniform holes and antenna-hole coupling
System can be made with virtually no dead-time
Simpler data volume may allow no “store and forward” (live imager)

## Slide 24: Thank You
Kael Hanson
10 km

## Slide 25: Supplemental Slides

## Slide 26: TDA / WASP/ Array Nominal Sensitivity Pattern
Air/Firn
Refraction
of Sky waves
Cos θ
Firn modeled as homogeneous, n=1.5
radio-transparent layer above sensors
First-order approximation for sub-firn, vertical dipole sensors

## Slide 27: Sensor Prototyping for SP 2010-11
Active Antenna Transient “Sensor”
Azimuthal symmetry with cable pass-through
Designed for RAM Drill (uniform 4” hole)
Ferrite
Ferrite
Ferrite
Ferrite
Ferrite
Ferrite