## Slide 1
Cascades in GVD
Zh.-A. Dzhilkibaev, INR (Moscow),
for the Baikal Collaboration
MANTS-2016, October 01, 2016

## Slide 2
Gigaton Volume Detector (Lake Baikal)
GVD array
Cluster

## Slide 3
Nominal PMT gain 1107 (PMT voltage 1250 – 1650 V)
Amplifier, kamp=10;
Pulse width ~20 ns
ADC: 12 bit 200 MHz FADC (5 ns time bin);
Waveform information is recorded in a programmable interval (up to 30 mks)
Linearity range: 1 ─ 100 p.e.;
Measuring channel
Time, 5 ns
A, mV
PMT
Amplifier
FADC
90 m coax.cable
Optical module
Central module

## Slide 4
Triggering and Data Transmission
SECTION
CLUSTER
2015: Coincidence
of neighbouring OMs
L/H = 1.5 p.e/4 p.e

## Slide 5
First Demonstration Cluster “Dubna”
(April 2015)
String section, 12 OMs
R ~ 40 m
L~ 345 m
192 OMs at 8 Strings
2 Sections per String
12 OMs per Section
DAQ-Center
Cable to Shore
Acoustic Positioning
System
Instrumentation String
with detector calibration
and environment moni-
toring equipment
Two LED beacons for
interstring calibration
Active depth 950 – 1300 m
Instrumented volume 1.7 Mt
Cable MEOC
- OE Cable Buoy Station
- Instrumentation string
- DAQ center
Final Layout

## Slide 6
Operation in 2015 yr.
(24 March – 10 February) - 294 days
Operation: 213 days
Efficiency: 72 %
Runs: 622
Data: 1.6∙109 events
Event rate ~ 100 Hz
Life time ~ 184 days
Configuration (24.10-17.12)
7 strings
different configurations during runs
Data sample
Dates 24.10.2015 – 17.12.2016
Life time 41.64 days
Statistics 437 970 024 events
trigger: coincidence of two neighboring OMs
with thresholds low&high = 1.5p.e.&4p.e.
Cumulative number of records

## Slide 7
Cascades Detection Mode
Cherenkov radiation
cascades
muon
Cascades from νe,τ & νμ(NC):
Point-like, strongly anisotropic
  light-source
  - cascade size proportional to ~lnE 
  (but LPM-effect for >20PeV!)
Light intensity proportional
to neutrino energy ~ E∙ 108 γ/TeV
Detection efficiency strongly
  depend on environment
  properties (water/ice).
  Angular resolution ~3°/15° (w/i)
  High energy resolution ~10-20%
Cascade curve

## Slide 8: „Big Bird“ ~ 2 PeV
IceCube
Notes: 2000 + 260 -240 1140 + 140 -130 1040 + 130 -145

## Slide 9
Shower 1.9 PeV,  = 116°,  = 23 m, z = -85 m
Cluster 2015
MC

## Slide 10
Neutrino Effective Area
IceCube
Demonstration Cluster
(GVD)
Scl ~ (0.05 - 0.1) SIC

## Slide 11
Cluster performance for cascade’s detection
Reconstruction of a cascade vertex:
Iterative procedure- OMs with
residual δt > 15 ns are excluded
and final Nhit is obtained for
following analysis.
δr = |rrec – rgen| ~ 2 m
(median value)
Distance between generated and
reconstructed vertices
Energy resolution :
δE/E ~ 30%
averaged by E-2 e spectrum
Averaged by E-2
e spectrum
Averaged by E-2
e spectrum
Nhit > 10
Nhit > 10

## Slide 12
Directional resolution for cascades:
~ 3°- 4° - median value of mismatch angles
Distribution of mismatch angles
Cumulative distribution
Nhit > 10
Nhit > 10

## Slide 13
Energy spectrum of astrophysical neutrinos
measured by IceCube:
1.2∙10-8 E-2 GeV-1 cm-2 s-1 sr -1
4.1∙10-6 E-2.46 GeV-1 cm-2 s-1 sr -1
Expected number of detected events in Demonstration Cluster
from astrophysical neutrinos for 1 yr. observation
Event selection criteria (Esh >100 TeV, Nhit >20):
0.4 – 0.6 events/yr - depending on a spectrum, background
conditions, and selection criteria
Nhit > 20 OM

## Slide 14
A search for cascades induced by
astrophysical neutrinos
(analysis of 2015 data – PRELIMINARY!)
Total number of accumulated events – 437 970 024 events
(thresholds: low/high = 1.5/4 ph.el.)
Life time – 3 597 921 s = 41.6 days
After causality cuts – 18 840 822 events
(Nhit > 3; |ti-tj| < Δrij/v + δt)

## Slide 15
Hit OMs multiplicity
Background muon bundle event
Water light-background

## Slide 16
Hit OM multiplicity dependence on cuts
Cuts | Events | Rejection
Reconstruction of shower coordinates | 1 171 077 | 1
(χ2 < 2) & (ρ <150 m; -272m < z < 200 m) | 316229 | 1/3.7
(La < 10)&(η > 0) | 12931 | 1/90
E > 30 TeV | 1291 | 1/900
Nhit > 20

## Slide 17
Hit OMs multiplicity after all cuts
Cuts | Events | Rejection
E > 30 TeV | 1291 | 1/900
E > 60 TeV | 859 | 1/1360
E > 100 TeV | 539 | 1/2000
One event with Nhit = 17 OMs and E > 100 TeV !

## Slide 18
Reconstructed energy of selected events
Hit OM multiplicity vs reconstructed energy
E > 30 TeV
Nhit > 10

## Slide 19
Reconstruction of shower vertex
All events
12931 ev.
E > 30 TeV
1291 ev.
E > 100 TeV
539 ev.

## Slide 20
Promising event (e584:8566299)
E = 158 TeV, θ = 59°, ρ = 73 m, z = -62 m
shower



## Slide 21
Arrival times of hit OMs
Str.8
Amplitude vs time
Run e584, event #8566299
Amplitudes of hit OMs

## Slide 22
Hit OMs multiplicity after all cuts

## Slide 23
Thank you!